## Slide 1
ECE 419/619 Electric Machines and Drives Induction Motor Drives
Scalar Control

## Slide 2: Volts per Hertz Control (Chapter 14)
Also called
V by f or V/Hz
scalar control
Low cost / Low performance
Simple microprocessor implementation
Usually doesn’t involve a speed sensor (open loop)

## Slide 3: Speed Control Through Stator Frequency

## Slide 4: Control of Voltage Vs*
constant
keep constant
to avoid saturation
where wb is the base
(or rated) electrical frequency
and Vb is rated Vs

## Slide 5: V/Hz Control

## Slide 12: Drive Limits
frequency: from 0 to 160% of rated
voltage: from 0 to rated

## Slide 13: Low-Frequency Boost
at low frequencies, rs becomes significant, then Vas ≠ jweLM
boost commanded
voltage at low
frequencies
~ ~

## Slide 14: Volts per Hertz Control for IM Drives
Straightforward, low-cost, low performance control typically without rotor speed measurement feedback
Commanded voltage is set proportional to commanded frequency in order to keep magnetizing flux at rated value; avoid saturation
Voltage is boosted at low frequencies to overcome stator resistance voltage drop

## Slide 15: Maximum Efficiency Control
With current regulation: Chapter 14
With voltage-source modulation: B.T. Branecky and K.A. Corzine, "Power Factor Control for Increased Induction Motor Efficiency," Frontiers of Power Conference, pages VII-1 - VII-9, Stillwater OK, October 1998.

## Slide 16: Efficiency From Steady-State Model

## Slide 19
for maximum efficiency

## Slide 20: Maximum Efficiency Control Example

## Slide 21: Maximum Efficiency Control
Note: Power factor has an inverse relationship with voltage.
A closed-loop control can be set up based on power factor.

## Slide 22: Control Diagram
Sensors
Is - rms (not instantaneous)
Vdc - average (not instantaneous)
Idc - average (not instantaneous)

## Slide 23: Control Diagram
Commanded power factor
Commanded frequency
Power factor calculation

## Slide 29: Maximum Efficiency Control for IM Drives
Type of IM control where the slip is set based on maximum efficiency
Chapter 14: Maximum efficiency control using current-regulated drive
Voltage-source drive can be used by regulating the power factor to its ideal value (based on slip for maximum efficiency)